## Slide 1
模拟电子技术基础
Analog Device
1.2 Diode 二极管
Qingfeng Zhang 张青峰
Department of Electrical and Electronic Engineering

## Slide 2
1.2 Diode 二极管
Diode: connect PN junction with wires and seal with shell.
P
N
阳极
阴极
Anode
Cathode

## Slide 3
Surface contact diode面接触型
Point contact diode点接触型
Anode
N-type Si
PN junction
Cathode
Au-Sb Alloy金锑合金
Base support底座
Al alloy
Anode
Cat whisker 触丝
Shell
N-type Ge
Cathode
1.2.1 Types of diode

## Slide 4
Planar diode平面型
N-Si
P-Si
SiO2 protection layer
Anode
Cathode

## Slide 5
1.2.2 Volt-ampere characteristics 伏安特性
+
u
P
N
-
Anode
Cathode
+
-
Anode
Cathode
P
N
+
-
u

## Slide 6
u
u
i
+
-
Anode
Cathode
P
N
击穿特性
IS
IS : reverse current
UT =KT/q: thermal voltage
T=300K, UT=26 mV
Forward
Reverse
Reverse Breakdown

## Slide 7
Forward
Reverse
正向特性
死区
Forward characteristic
Breakdown

## Slide 8
Forward
Reverse
Diode | Threshold voltage UON | Working voltage U | 
Si |  | 0.6~0.8 V | 0.7 V
Ge |  | 0.1~0.3 V | 0.2 V
Forward characteristic
Breakdown

## Slide 9
反向特性
Reverse characteristic
Diode | Is
Si | <0.1 mA
Ge | Order of 10 mA
Forward
Reverse
Breakdown

## Slide 10
|u|>|UBR|，current increases dramatically and enter the reverse breakdown region.
If the reverse current is not too large, the diode can still work.
Reverse breakdown
Forward
Reverse
Breakdown

## Slide 11
u
i
Reverse
Breakdown
IS
UBR
If the current is too large, the temperature of diode increases significantly, and diode breaks down permanently.
Diode | Breakdown temperature
Si | 150~200 oC
Ge | 75~100 oC
Zener breakdown齐纳击穿
Avalanche breakdown雪崩击穿
Breakdown mechanism：
Reverse breakdown

## Slide 12
Avalanche breakdown雪崩击穿
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
P
N
Internal electric field E
+
-
Minor carriers are accelerated to a very high speed and energy.
Accelerated electrons will collide with bonded electrons and kick them out.
More and more carriers are generated and current increases dramatically!

## Slide 13
Avalanche breakdown雪崩击穿
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
P
N
Internal electric field E
+
-
The condition for observing the avalanche breakdown:
Depletion region is wide.
Low doping concentration.

## Slide 14
雪崩击穿 Avalanche breakdown
通过空间电荷区的电子和空穴，会在电场作用下，使获得的能量增大。在晶体中运行的电子和空穴将不断的与晶体原子发生碰撞，通过这样的碰撞可使束缚在共价键中的价电子碰撞出来，产生自由电子-空穴对。新产生的载流子在电场作用下撞出其他价电子，又产生新的自由电子和空穴对。如此连锁反应，使得阻挡层中的载流子的数量雪崩式地增加，流过PN结的电流就急剧增大击穿PN结，这种碰撞电离导致击穿称为雪崩击穿。
半导体的掺杂浓度低
耗尽层宽，击穿电压相对高
条件
击穿电压具有正的温度系数
击穿电压高于6V
击穿的的特点

## Slide 15
Zener breakdown 齐纳击穿
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
P
N
Internal electric field E
+
-
In highly doped PN junction, the depletion region is narrow.
When E is large enough, the bonded electrons can be directly pulled out by the strong electric field.
Large amount of free electrons are generated and current increases dramatically!

## Slide 16
齐纳击穿 Zener breakdown
半导体的掺杂浓度高
耗尽层窄，击穿电压相对低
条件
击穿电压具有负的温度系数
击穿电压低于4V
击穿的的特点
当反向电压增大到一定程度时，空间电荷区内就会建立一个很强的电场。这个强电场能把价电子从共价键中拉出来，从而在空间电荷区产生大量电子-空穴对。这些电子-空穴对产生后，空穴被强电场驱到P区，电子被强电场驱到N区，使反向电流猛增。这种由于强电场的作用，直接产生大量电子-空穴对而使反向电流剧增的现象叫做齐纳击穿。

## Slide 17
u
i
Forward
Reverse
IS
Temperature ↑
Threshold voltage UON ↓
Reverse current IS ↑
UON
Temperature effect on the volt-ampere characteristics

## Slide 18
1.2.4 The model of diodes: forward
Ideal diode
u
i
Real
Ideal
理想二极管
The symbol for ideal diode
+
-

## Slide 19
Real
u
i
Ideal
UON
UON
Constant-volt model 恒压模型
Q: The symbol?
+
-

## Slide 20
u
i
UON
Broken-line model 折线模型
UON
Q: what’s the symbol?
Slope: G

## Slide 21
u
i
UON
Slope: G
Q
Question: what’s the DC and AC resistance at Q point?
AC/dynamic resistance: voltage/current signal is AC
u
DC/static resistance: voltage/current signal is DC
time
DC signal
AC signal

## Slide 22
u
i
UON
Broken-line model 折线模型
UON
Slope: G
AC resistance
DC source

## Slide 23
u
i
Du
Di
小信号模型、微变模型
Q
Small signal model
This model is only for AC signal.
AC/dynamic resistance at Q point:
Thermal voltage 热电压

## Slide 24
Example:
R=800W
UON=0.7V, rD=200W
U
[Q1] Using the broken-line mode, ask: when U= 0.5V, 1.7V, and -1.3V，the current in the circuit？
R=800W
U
UON
rD
R+rD
U-UON

## Slide 25
R+rD=1kW
U-UON
1. U=-1.3V，U-UON=-2V，i=0;
u
i
Ideal diode
2. U=0.5V，U-UON=-0.2V，i=0;
3. U=1.7V，U-UON=1V，i=(U-UON)/(R+rD)=1mA;

## Slide 26
V1
13 V
11 V
V2
R
10 kW
UAB
B
+
_
D2
A
D1
(a)
V1
13 V
11 V
V2
R
10 kW
UAB
B
+
_
D2
A
D1
(b)

## Slide 27
[Answer] How to judge diode on or off.
1. Assume diode is off, and analyze the circuit. If the uDiode>UON, diode is on. If the uDiode<UON, diode is off.
2. If there are two identical diodes D1 and D2 in the circuit，assume both diodes are off, and analyze the circuit. Compare uDiode1 with uDiode2. The diode with higher uDiode is on first. With one diode on, then judge the other diode.

## Slide 28
[Answer] 判断电路中二极管工作状态的方法
1. 断开二极管，分析电路断开点的开路电压。如果该电压能使二极管正偏，且大于二极管的开启电压，二极管导通；否则二极管截止。
2. 如果电路中有两个二极管，利用方法1分别判断各个二极管两端的开路电压，开路电压高的二极管优先导通；当此二极管导通后，再根据电路的约束条件，判断另一个二极管的工作状态。

## Slide 29
Fig.(a): voltage of D1, D2 is:
D1 on
ＵAB = 0 V
D2 off
11 V，–2 V
(a)

## Slide 30
Fig.(b): voltage of D1, D2 is:
Voltage of D1 is -13 V
D2 is on first
ＵAB = –13 V
D1 off
11 V，24 V
D2 is on:
(b)

## Slide 31
[Q3] D1 and D2 are ideal, the input voltage uI change from 0V to 30 V. Please draw the voltage transmission curve (uO ~ ui) 电压传输特性曲线.
+
_
uO
+
_
uI
5 kW
i1
R1
i2
R2
5 kW
6 V
18 V
V1
V2
D1
D2
iD1
iD2

## Slide 32
[Ans] Assume D1 and D2 are off:
When uI＜18 V，D2 is on first
When uI≤12 V，D1 off, D2 on:
When 12 V<uI<18 V，D1, D2 on
When 18 V ≤ uI，D1 is on first
The first method
D2 off
When D2 is on, voltage for D1:

## Slide 33
[Ans] Assume D1, D2 are on:
When D2 is on: uI＜18 V
When D1 is on: uI＞12 V
When uI≤12 V，D1 off, D2 on:
When 12 V<uI≤18 V, D1 on, D2 on
When 18 V<uI， D1 on, D2 off
The second method

## Slide 34
uO/V
uI/V
12
18
30
12
18
0
uO~uI curve

## Slide 35
uout
A
Application of diodes as rectifier
Input AC voltage signal:
u=Asin(wt)
二极管在整流电路的应用
R
u
+
-
Output AC voltage signal:
t
u
uout
Half-wave rectification
半波整流
A

## Slide 36
Input AC voltage signal:
u=Asin(wt)
t
u
uout
u
R
+
-
D1
D2
D3
D4
Full-wave rectification全波整流
uout
+
-

## Slide 37
Input AC voltage signal:
u=Asin(wt)
t
u
uout
u
R
-
+
D1
D2
D3
D4
Full-wave rectification全波整流
uout
+
-

## Slide 38
1.2.5 Voltage regulator diode 稳压二极管
u
i
Forward
Breakdown
Reverse
UZ
Working principle：
The reverse current change significantly, while the voltage is almost a constant. Hence it can stabilize the voltage.
Iz
I-V curve in breakdown region is very steep, which is almost parallel to y-axis.

## Slide 39
u
i
Forward
Breakdown
Reverse
UZ
Symbol of voltage regulator diode:
Iz
Anode
Cathode
DZ
Forward
UZ0
rZ
Equivalent circuit
D2
D1
Reverse
Anode
Cathode

## Slide 40
u
i
Forward
Reverse
UZ
Key parameters:
Iz
Anode
Cathode
2. Working voltage UZ：almost a constant
1. Working current IZ：Izmax > IZ > Izmin. Larger than Izmax: device breakdown permanently. Smaller than Izmin, the voltage stabilization effect becomes worse.
3. Dynamic resistance rZ: Smaller rz, better performance
Breakdown

## Slide 41
Working principle
Uin
+
_
Q: Input voltage Uin is unstable, and the bulb is flickering. How to resolve the problem？
R

## Slide 42
DZ
IZ
RL
Uout
Uin
R
I
Io
+
_
+
_
Uin
+
_
UZ
R
rZ

## Slide 43
DZ
IZ
RL
Uout
Uin
R
I
Io
+
_
+
_
rZ
UZ= UZ0 + IZrZ
UZ
+
_
IZ
RL
Uout
Uin
R
I
Io
+
_
+
_
UZ0
rZ
UZ
+
_

## Slide 44
DZ
IZ
RL
Uout
Uin
R
I
Io
+
_
+
_
UZ= UZ0 +IZrZ
DIoRL<< DI RL
Without regulator diode
With regulator diode
DUout=DIo RL
rZ
1st approach

## Slide 45
DZ
IZ
RL
Uout
Uin
R
I
Io
+
_
+
_
UZ= UZ0 +IZrZ
rZ
2nd approach
RL ↑
Uout ↑
UZ ↑
IZ ↑↑↑
I ↑↑↑
I R ↑↑↑
Uout= Uin-IR ↓
Negative feedback!

## Slide 46
[Q4] The working voltage of regulator diode is UZ，the maximum and minimum working current is IZMAX and IZMIN. Ask: the value of resistance R？
DZ
IZ
RL
Uout
Uin
R
I
Io
+
_
+
_
UZ
+
_

## Slide 47
DZ
IZ
RL
Uout
Uin
R
I
Io
+
_
+
_
UZ
+
_

## Slide 48
Application in Wireless Communication
Magnitude modulation
voice signal
carrier
Modulated Signal
Signal Modulation
O
t
u
u1
t
O
u2
O
t
amplifier
microphone
oscillator
modulator
transmitter
u2
u1
u

## Slide 49
Waveform Detection
u1
O
t
u2
O
t
O
t
u3
D
C
L
C2
u3
C1
R2
R1
u2
u1
+
–
+
–
+
–
amplifier
amplifier

## Slide 50
Varactor (变容二极管)
1. PN Junction: Cap. Effect
(1) Diffusion Capacitance CD
Forward Biased: unbalanced minor carriers
P
N
+
+
+
+
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
Major carriers in N zone diffusing to P zone become minor carriers, whose concentration decreases with distance.

## Slide 51
ΔU>0
3
ΔU=0
ΔU<0
2
1
x
Electron Concentration
3
2
1
P
N
+
+
+
+
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.

## Slide 52
Such an effect is presented by diffusion capacitance CD
Electron concentration is proportional to biased voltage
P
N
+
+
+
+
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.

## Slide 53
(2) Barrier Capacitance CB
U
P
N
+
+
+
+
+
+
+
+
Space Charge Region

## Slide 54
PN Junction gets narrower
Total charges decrease
a. As the biased voltage increases
U+U (U>0)
P
N
+
+
+
+

## Slide 55
PN Junction gets wider
Total charges increase
b. As the biased voltage decreases
Thus, the total charges change with the biased voltage
Such an effect is presented by barrier capacitance CB
U-U (U>0)
P
N
+
+
+
+
+
+
+
+
+
+
+
+

## Slide 56
Summary
Junction Capacitance Cj
Cj = CD + CB
Forward biased
Reverse biased

## Slide 57
Varactor: Symbol and C-U Curve
Symbol
20
2
40
60
80
100
0
4
6
8
10
12
uD
C
C-U Curve

## Slide 58
Homework: 1.1: 1.3, 1.4, 1.6