## Slide 1
模拟电子技术基础
Analog Device
2.1 Bipolar Junction Transistor
晶体三极管
Qingfeng Zhang 张青峰
Department of Electrical and Electronic Engineering

## Slide 2
2.1 Bipolar junction transistor (BJT)
Transistor is short for “Bipolar junction transistor”
双极型晶体管，又称半导体三极管，简称为晶体管
The amplification and switching functions of transistors have promoted the leap of electronic technology

## Slide 3
2.1.1 Structure of BJT
Transistor is made of two PN junctions: NPN or PNP
N
P
N+
e
b
c
e
N+
P
N
Emitter
发射极
Collector集电极
c
Base
基极
b
发射结
Emitter junction
BE junction
集电结
Collector junction
BC junction

## Slide 4
NPN transistor
NPN
e
b
c
e
N+
P
N
Emitter
发射极
Collector集电极
c
Base
基极
b
发射结
Emitter junction
BE junction
集电结
Collector junction
BC junction

## Slide 5
e
P+
N
P
Emitter
发射极
Collector集电极
c
Base
基极
b
发射结
集电结
PNP
PNP transistor
e
b
c
Emitter junction
BE junction
Collector junction
BC junction

## Slide 6
e
N+
P
N
Emitter
Collector
c
Base
b
发射区掺杂浓度大，面积小。
Key features of transistor（for amplification）：
集电区掺杂浓度低，集电结面积大。
基区掺杂浓度很低，且很薄。
（1）Emitter region: high doping, small area
（2）Collector region: low doping, large area
（3）Base region: low doping, very thin
NPN
e
b
c

## Slide 7
2.1.2 Working principle of transistor (NPN)
Take NPN-type transistor as an example
放大状态
饱和状态
截止状态
Amplification
Saturation
Cutoff region
Operating status of transistors

## Slide 8
e
N+
P
N
c
b
1. Amplification mode: BE junction forward bias & BC junction reverse bias
放大模式: 发射结正向偏置，集电结反向偏置
VCC
RC
VEE
RE
共基极放大电路
Common-base amplification circuit
Common-emitter amplification circuit
e
N+
P
N
c
b
VCC
RC
VBB
RB
共射极放大电路

## Slide 9
共基极放大电路
2.1.3 Common-base amplification circuit
VCC
RC
VEE
RE
e
c
b
IB
IC
IE
UBE
UCB
IC
e
N+
P
N
c
b
VCC
RC
VEE
RE
IB
IE
UBE
UCB
+
-
+
-

## Slide 10
IC
e
N+
P
N
c
b
VCC
RC
VEE
RE
IB
IE
UBE
UCB
+
-
+
-
Forward bias of BE junction
BE junction：N+ region is highly doped and P region is lightly doped. The electron concentration in N+ region is much higher than the hole concentration in P region.
Major carriers dominate the conduction of BE junction.
BE junction becomes thin or disappear.
Electrons (major carrier) in N+ region diffuse to P region under electric field.
Electric field

## Slide 11
IC
e
N+
P
N
c
b
VCC
RC
VEE
RE
IB
IE
UBE
UCB
+
-
+
-
Forward bias of BE junction
BE结：N+区是高掺杂，P区是低掺杂， N+区电子浓度远大于P区空缺浓度，以N +区电子导电为主，空穴忽略不计
多数载流子导电为主；
BE间的PN结宽度变薄或消失
N+区的大量电子在外电场的作用下扩散到P区
Electric field

## Slide 12
IC
e
N+
P
N
c
b
VCC
RC
VEE
RE
IB
IE
UBE
UCB
+
-
+
-
Reverse bias of BC junction
BC junction: N and P regions are both lightly doped, the electron and hole concentration is very low, much smaller than the electron concentration drifted from N+ region.
Minor carriers dominate the conduction in BC junction.
BC junction becomes thicker.
Most electrons drifted from N+ region are accelerated by the electric field of BC junction and collected by the collector. Only small portion is collected by base.
Electric field

## Slide 13
IC
e
N+
P
N
c
b
VCC
RC
VEE
RE
IB
IE
UBE
UCB
+
-
+
-
Reverse bias of BC junction
BC结：N区和P区都是低掺杂， 电子和空穴浓度都很低，远小于从N+区漂移过来的电子浓度
少数载流子导电为主；
BC间的PN结宽度变厚
PN结内电场+外电场
从N+区漂移过来的电子在BC间的内点场和外电场作用下，大部分漂移到N区形成电流IC，少部分被基极收集形成电流IB。还有少部分电子与P区的空穴复合，但是可以忽略不计

## Slide 14
1. 放大机理
作用过程：

## Slide 15
2. 影响放大的因素
影响静态放大系数因素：
集电极和和基极面积比例；
发射区和基区的掺杂浓度比；
动态由静态决定！

## Slide 16
UBE的开关控制作用；
控制能够实现交直流转换；
小能量控制大能量的结构；
3. 放大的关键
思考：放大的交流能量从何而来？
举例：水流的控制
放大器→控制转换器

## Slide 17: How does an amplifier work?
William Shockley, Nobel-Prize winning co-inventor of the transistor (a revolutionary electronic amplifier dating from the 1940s) had a vivid way of explaining it:
“If you take a bale of hay (干草) and tie it to the tail of a mule (骡子) and then strike a match (火柴) and set the bale of hay on fire, and if you then compare the energy expended shortly thereafter by the mule with the energy expended by yourself in the striking of the match, you will understand the concept of amplification."

## Slide 18
IC
e
N+
P
N
c
b
VCC
RC
VEE
RE
IB
IE
UBE
UCB
+
-
+
-
IE=IC+IB
共基极直流放大系数
Q: Why common-b amplification coefficient is not defined as:
ICBO
ICBO：the reverse saturation current when emitter is open.
Common-b DC amplification factor
Electric field

## Slide 19
e
N+
P
N
c
b
VCC
RC
VBB
RB
共射极放大电路
2.1.4 Common-emitter amplification circuit
VCC
RC
VBB
RB
IB
IC
IE
IC
IE
IB
VCC> VBB

## Slide 20
e
N+
P
N
c
b
VCC
RC
VBB
RB
IC
IE
IB
IE=IC+IB
ICBO
Electric field
共射极直流放大系数
Common-e DC amplification factor

## Slide 21
Common-e amplification coefficient
Common-b amplification coefficient

## Slide 22
Question!
Why N+ region should be highly doped?
IC
e
N+
P
N
c
b
VCC
RC
VBB
RB
IE
IB
Why P region should be thin?
Why P region should be lightly loped?

## Slide 23
IC
e
N+
P
N
c
b
VCC
RC
VBB
RB
IE
IB
Assume P-region is very thick
Internal and external electric field

## Slide 24
IC
e
N+
P
N
c
b
VCC
RC
VBB
RB
IE
IB
IC
e
N+
P+
N
c
b
VCC
RC
VBB
RB
IE
IB
P-region is highly doped
P-region is lightly doped

## Slide 25
IC
IE
IB
Common-base amplifier

## Slide 26
IC
IE
IB
Common-emitter amplifier

## Slide 27
VCC
RC
VBB
IC
IE
RB
e
c
b
RB
ui
+
-
IB
ib
ic
ie
uO
iB = IB + ib
Common-emitter AC amplification circuit
Total current
总瞬时电流
Direct current
直流电流
Alternating current
交流瞬时电流
交流复数值
交流有效值

## Slide 28
VCC
RC
VBB
IC
IE
RB
e
c
b
RB
ui
+
-
IB
ib
ic
ie
uO
Output DC voltage:
Output AC voltage:
Common-emitter AC amplification circuit
Output voltage (DC+AC):

## Slide 29
共射交流放大系数
Common-e:
Common-b:
In general case:
Common-emitter AC amplification coefficient
VCC
RC
VBB
IC
IE
RB
e
c
b
RB
ui
+
-
IB
ib
ic
ie
uO

## Slide 30
2．发射结正向偏置、集电结正向偏置—饱和状态
（2）IC ≠ bIB，IB失去了对IC的控制。
（1）UCB (=UCE-UBE)≤0。集电结零偏或正偏
饱和状态的特点
（3) 集电极饱和电压降UCES较小
小功率硅管0.3~0.5V。

## Slide 31
（5） UCE对IC的影响大，
当UCE增大，IC将随之增加。
当UCE增大使集电结从正偏往零偏变化过程中， UCE越大，到达集电区的非平衡少子就越多，Ic将随着UCE增大而增加。
（4）饱和时集电极电流

## Slide 32
（2） IC=ICBO，IB=－ICBO
3．发射结反向偏置、集电结反向偏置—截止状态
截止状态的特点：
（1） UBE小于死区电压。

## Slide 33
2.1.4 The input and output I-V characteristics
Input I-V characteristics:
iB
uBE
Common-emitter
iC
iE
e
c
b
uBE
+
-
iB
uCE
+
-
P
N+
N
uCE=0
1) When uCE=0, BE and BC junction are forward biased by uBE. The internal electric field is in BC junction is decreased, most electrons are collected by the Base. The I-V curve is similar to that of PN junction.

## Slide 34
Common-emitter
iC
iE
e
c
b
uBE
+
-
iB
uCE
+
-
uCE=0
0.5V
>1V
iB
uBE
2) When uCE increase (<1V), the electric field in BC junction increase. Some electrons are collected by Collector, and the left are collected by Base. To reach the same value of iB, uBE should be larger. Hence the I-V curve shifts to right.
P
N+
N
3) When uCE is large enough (>1V), the electric field in BC junction is strong enough, and most electrons are collected by Collector and Collector is saturated. Even further increase uCE, the curve does not shift any more.

## Slide 35
Saturation
Output I-V characteristic
iC
uCE
Common-emitter
iC
iE
e
c
b
uBE
+
-
iB
uCE
+
-
P
N+
N
iB=80mA
60mA
40mA
20mA
0mA
Cut-off 截止区
Amplification
1) Cut-off region：
uBE < UON threshold voltage
uCE > uBE

## Slide 36
Saturation
Common-emitter
iC
iE
e
c
b
uBE
+
-
iB
uCE
+
-
P
N+
N
iC
uCE
iB=80mA
60mA
40mA
20mA
0mA
Cut-off
2) Amplification region放大区：
uBE > UON
uCE > uBE
BC junction is reverse biased
3) Saturation region饱和区：
uBE> UON
uCE< uBE
BC junction is forward biased
Amplification

## Slide 37
iC
iE
e
c
b
uBE
+
-
iB
uCE
+
-
P
N+
N
NPN
PNP
iC
iE
e
c
b
uBE
iB
uCE
N
P+
P
+
-
+
-
Amplification mode
Amplification mode
Question!

## Slide 38
2.1.5 Summary of key parameters of transistor
3) ICBO: when emitter is open, the reverse saturation current in BC junction
1) Common-b DC amplification factor:
2) Common-e DC amplification factor:
4) ICEO: when base is open, the reverse saturation current Between emitter and collector

## Slide 39
5) Common-b AC amplification factor:
6) Common-e AC amplification factor:
7) Cut-off frequency fT (will talk about his in the 4th chapters)

## Slide 40
Limit parameters 极限参数
4) Maximum current allowed in collector: ICM
1) The reverse breakdown voltage of BE junction U(BR)EBO
2) The reverse breakdown voltage of BC junction U(BR)CBO
3) The reverse breakdown voltage of CE junction U(BR)CEO

## Slide 41
5) The maximum power dissipation allowed in collector: PCM
Safe operation area
iC
uCE
ICM
U(BR)CEO
PCM=uCExiC
PCM determined the temperature of transistors. For Si transistor, T<150o. For Ge transistor, T<70o.

## Slide 42
Homework1-2:
1.8, 1.9, 1.10, 1.12
Diode | Threshold voltage UON | Working voltage U | 
Si |  | 0.6~0.8 V | 0.7 V
Ge |  | 0.1~0.3 V | 0.2 V