## Slide 1
模拟电子技术基础
Analog Device
3 Field-effect Transistor (FET)
场效应晶体管
(Chapter 1.4)
Qingfeng Zhang 张青峰
Department of Electrical and Electronic Engineering

## Slide 2
3.1 Field-effect transistors (FETs)
FET uses the electric field effect to control the output current
场效应晶体管，简称称场效应管，是利用电场效应来控制输出回路电流的一种半导体器件
Compare FET with BJT:
BJT (Bipolar junction transistor)双极型晶体管:
Current-controlled device 电流控制型器件
Input resistance is small
Both electrons and holes are involved in conduction

## Slide 3
FET 场效应晶体管:
High input resistance: 107 ~1015W
Only one type of carriers (electrons or holes) is involved in conduction
Small size, light, low-power consumption, long life span
Low noise, high stability, simple fabrication process
Widely used in large-scale integration circuits

## Slide 4
FET 场效应晶体管:
JFET (Junction Field Effect Transistor)
结型场效应管
2. IGFET (Insulated Gate Field Effect Transistor)
绝缘栅型场效应管

## Slide 5
BJT
JFET
3.2 JFET

## Slide 6
SiO2 protection layer
N-type JFET
Gate栅极
Drain漏极
Source源极
s
P+
N
g
d
g
P+
Depletion layer耗尽层
g
d
s

## Slide 7
SiO2 protection layer
P-type JFET
Gate栅极
Drain漏极
Source源极
s
N+
P
g
d
g
N+
Depletion layer耗尽层
g
d
s

## Slide 8
N-type JFET
s
P+
N
g
d
g
P+
When uGS=uDS=0:
g
d
s
uDS (VDD)
Depletion region is narrow, conduction channel is wide
uGS
(VGG)
uDS
(VDD)
uGS(VGG)

## Slide 9
When UGS(off)<uGS<0:
Depletion region becomes wider, conduction channel becomes narrower
The resistance RDS ↑
1) uDS=0
s
P+
N
g
d
g
P+
uDS (VDD)
uGS(VGG)

## Slide 10
When uGS< UGS(off):
Depletion regions are connected, conduction channel disappears
The resistance RDS is extremely large
UGS(off) is called gate pinch-off voltage 夹断电压
1) uDS=0
s
P+
N
g
d
g
P+
uDS (VDD)
uGS(VGG)

## Slide 11
Conduction channel becomes wedge-shaped
When 0<uDS<|UGS(off)|:
2) uGS=0
iD
The reverse voltage on PN is position-dependent
s
P+
N
g
d
g
P+
uDS (VDD)
uGS(VGG)

## Slide 12
When uDS=|UGS(off)|:
2) uGS=0
Pinch-off region is a point
点夹断(预夹断)
iD
s
N
g
d
g
uDS (VDD)
uGS(VGG)
P+
P+

## Slide 13
When uDS>|UGS(off)|:
2) uGS=0
Pinch-off region becomes wider and longer
夹断区延长
iD
s
N
g
d
g
uDS (VDD)
uGS(VGG)
P+
P+

## Slide 14
iD
s
N
g
d
g
uDS (VDD)
uGS(VGG)
P+
P+

## Slide 15
uDS and uGS will modify the channel shape together
When uDS=|UGS(off)|+ uGS
3) uGS<0，uDS>0
iD
s
N
g
d
g
uDS (VDD)
uGS(VGG)
P+
P+
or uDG=|UGS(off)|
The channel begins to pinch off

## Slide 16
3.2.1 JFET: I-V characteristics
g
d
s
uGS
(VGG)
uDS
(VDD)
iG
iD
Extremely high input resistance

## Slide 17
iD
uDS
uGS=0V
Cut-off region 夹断/截止区
uGS=-0.5V
uGS=-1V
uGS=-1.5V
uGS=UGS(off)
uDS=|UGS(off)|+ uGS
Variable resistor region可变电阻区
Constant current region恒流区
Output I-V curve

## Slide 18
Variable resistor region可变电阻区
Tunable by uGS
uDS is small, the channel are conducting
FET behaves like a resistance-tunable resistor
uDS<|UGS(off)|+ uGS
iD
uDS
uGS=0V
uGS=-0.5V
uGS=-1V
uGS=-1.5V
uGS=UGS(off)
uDS=|UGS(off)|+ uGS

## Slide 19
uDS is large, channel pinches off 沟道预夹断
Also can be called as amplification region
uDS≥ |UGS(off)|+ uGS
iD
uDS
uGS=0V
uGS=-0.5V
uGS=-1V
uGS=-1.5V
uGS=UGS(off)
uDS=|UGS(off)|+ uGS
Constant current region恒流区
iD is almost constant, only depends on uGS
也称作放大区

## Slide 20
Cut-off region 夹断/截止区
Channel fully pinches off
uGS < UGS(off)
iD
uDS
uGS=0V
uGS=-0.5V
uGS=-1V
uGS=-1.5V
uGS=UGS(off)
uDS=|UGS(off)|+ uGS

## Slide 21
iD
uDS
uGS=0V
uGS=-0.5V
uGS=-1V
uGS=-1.5V
uGS=UGS(off)
uDS=|UGS(off)|+ uGS
Transfer curve 转移特性曲线
iD
uGS
0
In variable resistor region, the transfer curves depend on uDS
In constant-current region, the transfer curves are independent of uDS
UGS(off)
-1.5V
-1V
-0.5V

## Slide 22
At constant-current region:
UGS(off)
uGS=0V
uGS=-0.5V
uGS=-1V
uGS=-1.5V
uGS=UGS(off)
uDS=|UGS(off)|+ uGS
iD
uGS
0
IDSS
uDS
iD
IDSS is the drain current at uGS=0, uDS>|UGS(off)|

## Slide 23
3.2.2 JFET: Key parameters
1) Pinch-off voltage UGS(off) 夹断电压
DC parameters 直流参数
2) Drain saturation current IDSS 漏极饱和电流
IDSS : The drain current at uGS=0, uDS>|UGS(off)|
3) DC Input resistance RGS 直流输入电阻
g
d
s
uGS
(VGG)
uDS
(VDD)
iG
iD

## Slide 24
1) Transconuctance gm 互导/跨导
AC parameters 交流参数
g
d
s
uGS
uDS
iG
iD
At constant-current region:
Larger IDQ, larger gm
2) There exists capacitance between drain, source and gate: Cgs, Cgd, Cds
In high frequency circuits, we need to consider Cgs, Cgd, Cds

## Slide 25
1) Maximum drain current IDSM
Absolute maximum ratings 极限参数
2) Maximum drain dissipation power PDSM
最大漏极电流
漏极最大耗散功率
3) Gate breakdown voltage U(BR)GS
栅极击穿电压
4) Drain-source breakdown voltage U(BR)DS
漏源击穿电压
g
d
s
uGS
uDS
iG
iD

## Slide 26
Q1: As shown in the figure，FET has UGS(off)=-5V；Ask: In the three situations listed below, FET works in which region?
1) uGS=-8V, uDS=4V
2) uGS=-3V, uDS=4V
3) uGS=-3V, uDS=1V
1) uGS<UGS(off), in cut-off region
Answer:
iS
g
d
s
VGG
uDS
iG
iD
VDD
RD
RG
+
_
+
_
uGS
2) uDS>|UGS(off)|+uGS, in constant-current region
3) uDS<|UGS(off)|+uGS, in variable resistor region

## Slide 27
3.3 IGFET
IGFET (Insulated Gate Field Effect Transistor)
绝缘栅型场效应管
Enhancement mode
增强型
Depletion mode
耗尽型
N-type
P-type
N-type
P-type

## Slide 28
3.3.1 Enhanced N-type IGFET
s
P
g
d
B
SiO2 insulated layer
Gate栅极
Drain漏极
Source源极
N+
N+
JFET
MOSFET
Metal
Oxide
Semiconductor
IGFET is also called:

## Slide 29
Working principle:
s
P
g
d
B
N+
N+
uGS
uDS
iD

## Slide 30
s
P
g
d
B
N+
N+
uGS=0
uDS
iD
One PN junction is reversed
iD=0

## Slide 31
s
P
g
d
B
N+
N+
uGS
uDS
iD
Gate-SiO2-Semiconductor can be treated as a parallel-plate capacitor 平行板电容器
Electrons are attracted and holes are repulsed to SiO2 surface

## Slide 32
Gate-SiO2-Semiconductor can be treated as a parallel-plate capacitor 平行板电容器
Electrons are attracted and holes are repulsed to SiO2 surface
s
P
g
d
B
N+
N+
uGS
uDS
iD
Inversion layer (反型层) is formed near SiO2 surface

## Slide 33
s
P
g
d
B
N+
N+
uGS
uDS
iD
Enhanced N-type IGFET is also called NMOS

## Slide 34
The electric field in SiO2 is larger
s
P
g
d
B
N+
N+
uGS
uDS
iD

## Slide 35
s
P
g
d
B
N+
N+
uGS
uDS
iD
The potential of channel near drain is smaller
The electric field in SiO2 near drain is smaller
The conducting channel is wedge-shaped 楔形

## Slide 36
s
P
g
d
B
N+
N+
uGS
uDS
iD
Channel begins to pinch off 沟道预夹断
NMOS begins to enter the constant current region

## Slide 37
s
P
g
d
B
N+
N+
uGS
uDS
iD
The pinch-off region extends 夹断区延长
NMOS is in constant current region

## Slide 38
s
P
g
d
B
N+
N+
uGS
uDS
iD

## Slide 39
iD
uDS
Cut-off region 夹断/截止区
uGS=UGS(th)
uDS= uGS - UGS(th)
Variable resistor region可变电阻区
Constant current region恒流区
Output I-V curve
uGS>UGS(th)

## Slide 40
Variable resistor region可变电阻区
iD
uDS
uGS=UGS(th)
uDS= uGS - UGS(th)
Tunable by uGS
uDS is small, the channel are conducting
FET behaves like a resistance-tunable resistor
uDS< uGS - UGS(off)

## Slide 41
iD
uDS
uGS=UGS(th)
uDS= uGS - UGS(th)
Constant current region恒流区
uDS is large, channel pinches off 沟道预夹断
Also can be called as amplification region
iD is almost constant, only depends on uGS
uDS ≥ uGS - UGS(th)
uGS ≥ UGS(th)

## Slide 42
iD
uDS
uGS=UGS(th)
uDS= uGS - UGS(th)
Channel fully pinches off
uGS < UGS(th)
Cut-off region 夹断/截止区

## Slide 43
iD
uDS
uGS=UGS(th)
Transfer curve 转移特性曲线
iD
uGS
0
In constant-current region, the transfer curves are independent of uDS
uDS= uGS - UGS(th)
uGS=2UGS(th)
UGS1
UGS2
UGS3
UGS(th)
2UGS(th)

## Slide 44
iD
uDS
uGS=UGS(th)
iD
uGS
0
uDS= uGS - UGS(th)
uGS=2UGS(th)
UGS1
UGS2
UGS3
UGS(th)
2UGS(th)
At constant-current region:
IDO is the drain current at uGS=2UGS(th)
IDO

## Slide 45
3.3.2 Depleted N-type IGFET/MOSFET
SiO2 are doped with positive ions
There is an inversion layer even when uDS=0 and uGS=0
s
P
g
d
B
SiO2 insulated layer
N+
N+
+
+
+
+
+
+
+
+
+
+
uGS=0
uDS
iD
Hence, when uDS>0 and uGS=0, iD>0

## Slide 46
The inversion layer becomes wider
s
P
g
d
B
N+
N+
+
+
+
+
+
+
+
+
+
+
uGS
uDS
iD
The inversion layer becomes narrower

## Slide 47
Output I-V curve
iD
uDS
uGS=UGS(th)>0
uDS= uGS - UGS(th)
uGS=2UGS(th)
UGS1
UGS2
UGS3
iD
uDS
uGS=UGS(off)<0
uDS= uGS - UGS(off)
uGS=0
Enhanced NMOS
Depleted NMOS

## Slide 48
Transfer curve 转移特性曲线
iD
uGS
0
UGS(th)
UGS(off)
Enhanced NMOS
Depleted NMOS

## Slide 49
3.3.3 Summary
JFET
g
d
s
N
g
d
s
P
Enhanced MOSFET
Depleted MOSFET
s
g
d
N
B
g
d
s
P
B
g
d
s
N
B
g
d
s
P
B

## Slide 50
FET 场效应晶体管 (Compared with BJT)
1) FET: Use voltage uGS to control current iD
BJT: Use current iB to control current iC
Gate(栅极), source(源极), and drain(漏极) in FET corresponds to the base(基极), emitter(发射极), and collector(集电极) in BJT
BJT: Low input resistance REB

## Slide 51
4) FET: Small size, light, low-power consumption, long life span
3) FET: Only one type of carriers (electrons or holes) is involved in conduction
BJT: Both electrons and holes are involved in conduction
5) FET: The device structure is symmetric, hence source and drain can be exchanged
6) FET: The size of FET is only about 5% of that of BJT. Hence it is widely used in large-scale integration circuits

## Slide 52
8) FET: FET is more vulnerable to environment electrostatic charges. The high input resistance and ultra-thin insulating layer make charges accumulate in FET, and breakdown the insulating layer. 由于MOS管的输入电阻高，由外界感应产生的电荷不易泄露，而栅极上的绝缘层又很薄，这将在栅极上产生很高的电场强度，以致引起绝缘层的击穿而损坏管子。
7) FET: The transconductance is smaller than that of BJT. With similar load resistance, the voltage gain is usually smaller than that of BJT.